## Slide 1: Optimizing SpMV in accordance with HPCG Benchmark
Presented By:
Ahmed Abdullah
Mohammad Rohaan
Presented To:
Muhammad Rizwan

## Slide 2
High
Performance
Conjugate
Gradient
Designed for real-world workloads
Focuses on:
  Memory access
  Sparse computations
  Iterative solvers
More realistic than HPL (Linpack)

## Slide 3: Why
1
HPCG is Important
Real reason applications use:
  Memory access
  Sparse computations
  Iterative solvers
More realistic than HPL (Linpack)
  Climate models
  Structural simulations
  CFD problems
HPCG Simulates:

## Slide 4
Main Kernels in HPCG
SpMV (Sparse Matrix-Vector Multiplication)
SymGS(Symmetric Gauss-Seidel)
Multigrid(MG.)
Dot Product
Vector Updates(WAXPBY)

## Slide 5: Why we selected SpMV
Memory Bandwidth limited
Most time consuming Kernel
Appears in every CG iteration
Small Improvements bring
meaningful Impacts

## Slide 6: Our process is easy
=
A
x
Y
Sparse Matrix
Input Vector
Output Vector
SpMV multipies a sparse matrix
with a vector, which is the core operation
in the CG solver

## Slide 7: Our Optimisation Strategy
We utilized 4-way loop Unrolling:
  Reduces loop overhead
  Improves register reuse
  Better instruction-level parallelism
No change in data structures
This project is inspired by CVR: Efficient Vectorization of SpMV on x86 processors, which focuses on improving Sparse Matrix-Vector Multiplication using vectorization and cache-friendly memory access. Instead of implementing the full CVR format, a simpler loop-unrolling optimization was applied to the HPCG SpMV kernel.

## Slide 8: Where the Code was Modified
Src/ComputeSPMV-ref.cpp
Inner SpMV loop
optimized
HPCG components unchanged

## Slide 9
4000
3000
2000
1000
0
System Architecture
Intel Core i5-5300U
@2.30 GHz
2 core
Processor w/
4 Threads
8
GB RAM
Running Linux
(WSL)

## Slide 10: Experimental Setup
Grid Size 16x16x16
Run-Time: 30 seconds
Two runs performed:
  Baseline: Original SpMV
  Optimized: Unrolled SpMV

## Slide 11: BASELINE PERFORMANCE
Metric | Value
SpMV Time | 24.6904s
SpMV GFLOP/s | 0.123072
Total Time | 157.837s
Total GFLOP/s | 0.1307

## Slide 12: Optimized Performance
SpMV time: 24.4821s
SpMV GFLOP/s: 0.124118
Total time: 165.699s
Total GFLOP/s: 0.124442

## Slide 13: PERFORMANCE COMPARISON
Kernel-level Improvement achieved
SpMV became Faster
SpMV GFLOP/s Increased
Total HPCG Score slightly decreased

## Slide 14
WHY TOTAL HPCG SCORE DECREASED
HPCG includes:
SpMV is memory-bandwidth bound
CPU optimization alone gives limited global gains
  Multigrid
  Dot products
  Vector updates

## Slide 15: KEY LEARNING OUTCOMES
Understanding sparse matrix computation
Kernel-level optimzaion
HPCG benchmrk and System Architecture analysis
Benchmarking and Performance analysis

## Slide 16: CONCLUSION
  SpMV kernel successfully
  optimized
  Visible performance improvement
  Correctness preserved
Project objectives achieved

## Slide 17: Ideas for the future
SIMD Vectorization
    Cache Blocking
Data format optimizations (SELL, ELL, CSR)
Multithreaded SpMV

## Slide 18: Thanks!
Any questions?